## Slide 1
PATIENT-SPECIFIC ARTICULATED DIGITAL TWINS
from a Single Full-Body CT Scan
Authors: Han Zhang, Boyang Zhao, Mathias Unberath Affiliation: Johns Hopkins University, Baltimore, USA Source: arXiv:2607.02156v1 [cs.CV], 2026
Presented by: Atharva R. Gosavi (Roll No. 252SP009) Programme: M.Tech. SPML, Dept. of Electronics & Communication Engineering Guide: Prof. Amareswararao Kavuri
Synthetic Radiography · Surgical Planning · Patient Modeling
Patient-Specific Articulated Digital Twins | Slide 1 of 7
Notes: Good morning/afternoon. I am presenting the paper 'Patient-Specific Articulated Digital Twins from a Single Full-Body CT Scan' by Zhang, Zhao and Unberath from Johns Hopkins University. In short, this paper shows how to take one CT scan and turn it into a digital patient model that can be moved into different body poses.

## Slide 2
Why Do We Need a Digital Twin of a Patient?
Introduction & Real-World Motivation
The Problem
A CT scan captures a patient's body in only ONE position (lying flat). It cannot show how the same anatomy would look if the patient moved or was repositioned.
Why It Matters
In real hospitals, X-rays and surgeries need the patient in different poses. A frozen, single-pose model cannot help plan or simulate this.
Real-Life Use
Surgical planning, image-guided procedures, positioning studies, and training AI models on realistic X-ray images all need pose-flexible anatomy.
Static CT vs. Articulated Twin
Fixed pose
(scan-time only)
Any pose
(posable twin)
A patient scanned once (supine) can be virtually re-posed — standing, arms raised, bending — while keeping their OWN real anatomy.
Takeaway: This paper turns a single static CT scan into a posable, patient-specific digital twin.
Patient-Specific Articulated Digital Twins | Slide 2 of 7
Notes: A CT scan freezes the patient in one position. But in real hospitals, X-rays and surgeries need many positions. Population phantoms can change pose but aren't the real patient; CT-based simulations are patient-specific but frozen. This paper's goal is to get both properties at once.

## Slide 3
Problem Statement & Motivation
What existing methods get wrong, and the gap this paper fills
Approach | Patient-Specific? | Posable? | Key Drawback
Population phantom (e.g., XCAT) | ✗ No | ✓ Yes | Uses a generic template body, not the real patient anatomy
CT-derived DRR simulation | ✓ Yes | ✗ No | Anatomy is frozen in the pose captured at scan time
Proposed Articulated Twin | ✓ Yes | ✓ Yes | Proof-of-concept, tested on only 3 subjects so far
Motivation Flow
Gap identified
No model is both patient-specific AND posable
Idea
Fuse CT anatomy with a posable body model (SMPL)
Proposed work
Articulated digital twin from ONE CT scan
Why is this important? Existing radiographic simulation can change the CAMERA angle but not the PATIENT's body position — this paper fixes that.
Patient-Specific Articulated Digital Twins | Slide 3 of 7
Notes: Table compares three approaches. XCAT phantoms are posable but generic. CT-derived DRR simulation is patient-specific but frozen. The proposed twin is both, though it is currently only validated on 3 subjects. This gap in the literature is the direct motivation for the paper.

## Slide 4
Methodology: How the Digital Twin Is Built
Three stages turn a raw CT scan into a posable patient twin
1. Patient Anatomical
Modeling
TotalSegmentator labels bone, organs & body from CT
Marching Cubes + smoothing → 3D surface meshes
Fit SMPL body model (shape β, pose θ) to patient
Output: static twin in scan pose
2. Anatomy-Aware
Kinematic Binding
Build a skeleton tree rooted at the pelvis
Each bone rigidly linked to one joint (no blending)
Joint centers taken from real bone-to-bone contacts
Output: a patient-specific rig
3. Pose Retargeting
Pick a target pose (e.g., from motion-capture data)
Compute joint rotations from scan pose → target pose
Apply rotations rigidly to bones & organ groups
Output: reposed twin, renderable as a new X-ray
The Fitting Objective (in plain terms)
L = λchamfer·(match outer body shape) + λinclusion·(keep bones INSIDE the body) + λprior·(keep pose realistic)
Simple idea: the fitted body "envelope" is optimized to fully enclose the patient's real bones — enclosing the skeleton matters more than perfectly matching the skin surface, because CT is scanned lying down while the body model assumes standing.
Patient-Specific Articulated Digital Twins | Slide 4 of 7
Notes: Three stages: (1) segment the CT and fit a parametric SMPL body model around the patient's real bones; (2) bind each bone rigidly to a joint, unlike normal smooth-skin animation; (3) retarget a new target pose onto the rig using forward kinematics. The loss function balances matching body shape, keeping bones inside the body, and keeping the pose realistic -- enclosure is prioritized over surface accuracy.

## Slide 5
Worked Example: One Patient, Start to Finish
Following a single CT scan through all five stages of the pipeline
Full-Body CT Scan
Patient lies flat and is scanned once
Segmentation
TotalSegmentator labels bones, organs & skin
Patient Digital Twin
SMPL body fitted around the real skeleton
Reposed Twin
Retarget to a new pose, e.g. arm raised
Synthetic X-Ray
DRR rendered in the NEW pose
What's Really Happening Here?
Think of the skeleton as LEGO bricks and the SMPL body model as a stretchy glove that fits around them.
The glove is first shaped to exactly match how the patient was lying during the scan.
To change the pose, we tell the glove "raise the right arm" — and because each bone is rigidly attached to a joint, the real bones move together, exactly like a puppet's skeleton, without warping.
The result is rendered as a new, physically-consistent synthetic X-ray for the new pose — something a single CT scan alone could never show.
Patient-Specific Articulated Digital Twins | Slide 5 of 7
Notes: Walk through one patient end to end: CT scan, segmentation, the fitted digital twin at the scan pose, the same twin retargeted to a new pose such as a raised arm, and finally a synthetic X-ray rendered from that new pose. Emphasize the LEGO-and-glove analogy: bones are rigid pieces, SMPL is the flexible outer layer that carries the motion.

## Slide 6
Results: How Good Is the Digital Twin?
Evaluated on 3 full-body CT subjects from the NMDID dataset
Region | Chamfer (mm) ↓ | Enclosure (%) ↑ | SSIM ↑ | PSNR (dB) ↑
Upper body | 15.7 ± 2.9 | 95.0 ± 2.4 | 0.890 ± 0.007 | 19.6 ± 1.3
Torso | 16.2 ± 3.5 | 94.1 ± 2.4 | 0.872 ± 0.026 | 17.5 ± 1.0
Lower body | 16.5 ± 4.8 | 99.0 ± 0.4 | 0.855 ± 0.035 | 18.4 ± 2.6
Overall | 15.8 ± 4.0 | 95.9 ± 1.8 | 0.872 ± 0.016 | 18.5 ± 1.4
Chart: Skeletal Enclosure Stays High — Even in New Poses
| Upper Body | Torso | Lower Body | Overall | Unseen Pose
Skeletal Enclosure (%) | 95 | 94.1 | 99 | 95.9 | 94.4
What Do These Numbers Mean?
Chamfer distance ~16 mm
Average gap between the fitted body surface and the real CT surface — small relative to a full-body scale.
Enclosure ~96%
96% of the real skeleton sits safely inside the fitted body envelope — the twin doesn't "lose" any bone.
SSIM 0.87
Synthetic X-rays closely match the structure of a real X-ray at the same pose (1.0 = identical).
Enclosure holds at 94.4% in NEW poses
Even after articulating into 28 unseen poses, the rig stays intact — no skeleton "breaking out" of the body.
Patient-Specific Articulated Digital Twins | Slide 6 of 7
Notes: Explain each metric simply: Chamfer distance is average surface gap (~16mm, small at body scale). Enclosure (~96%) means almost all real bone stays inside the fitted body envelope. SSIM (0.87) and PSNR show the synthetic X-ray closely matches structure of a real one. Crucially, enclosure stays high (94.4%) even in 28 brand-new, unseen poses -- showing the rig does not break down when articulated.

## Slide 7
Conclusion & Future Work
From a single CT scan to a living, posable patient model
Key Contributions
First patient-specific twin that is both accurate AND posable
3-stage pipeline: fit → bind → retarget
Pose-dependent synthetic X-ray (DRR) generation
Limitations
Proof-of-concept tested on only 3 patients
Organs/soft tissue move as rigid blocks, not true deformation
Extreme poses may cause hand/joint mismatches
Future Work & Applications
Larger, more diverse patient cohorts
Clinically realistic positioning scenarios
Surgical planning, AI training data, image-guided intervention
A single CT scan no longer has to be frozen in time — it can become a dynamic, patient-specific twin that moves.
Patient-Specific Articulated Digital Twins | Slide 7 of 7
Notes: Summarize contributions, be upfront about limitations (only 3 subjects, rigid organ movement, extreme-pose artifacts), and close with future work and applications: surgical planning, generating synthetic training data for AI, image-guided intervention, and patient positioning studies. End with the one-line takeaway.